CONE MODEL C9 - CNC 3 AXIS SERVO DRIVE

BALL SCREW PRESS BRAKE

CAPACITY. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .25 TONS

BENDING LENGTH . . . . . . . . . . . . . . . . . . . . . . . . .34”

DISTANCE BETWEEN HOUSINGS . . . . . . . . . . .31.1”

STROKE LENGTH . . . . . . . . . . . . . . . . . . . . . . . . . .9.84”

MAXIMUM OPEN HEIGHT.. . . . . . . . . . . . . . . . . .19.7”

CLOSED HEIGHT. . . . . . . . . . . . . . . . . . . . . . . . . . .9.84”

THROAT DEPTH. . . . . . . . . . . . . . . . . . . . . . . . . . . .5.9”

RAM APPROACH SPEED . . . . . . . . . . . . . . . . . . . .236 IPM

RAM PRESSING SPEED . . . . . . . . . . . . . . . . . . . . .10 – 47 IPM

RAM REPEATABILITY IN PRESSING SPEED. +/-0.000079”

RAM RETURN SPEED . . . . . . . . . . . . . . . . . . . . . . .236 IPM

BACK GAUGE (X) TRAVEL . . . . . . . . . . . . . . . . . .15.7”

BACK GAUGE (X) SPEED . . . . . . . . . . . . . . . . . . . .1,181 IPM

BACK GAUGE (X) ACCURACY. . . . . . . . . . . . . . .+/-0.00098”

BACK GAUGE (R) HEIGHT MOVEMENT. . . . . .5.5”

BACK GAUGE (R) HEIGHT SPEED . . . . . . . . . . .236 IPM

BACK GAUGE (Z1,Z2) MOVEMENT . . . . . . . . . .4.7” – 26.4”

BACK GAUGE (Z1,Z2) SPEED. . . . . . . . . . . . . . . . 2,362 IPM

BACK GAUGE (Z1,Z2) ACCURACY. . . . . . . . . . . +/- .02”

BACK GAUGE (DELTA X) MOVEMENT . . . . . . +/- 2”

BED TOP WIDTH/HEIGHT. . . . . . . . . . . . . . . . . . . 2.75” @ 33.5”

MOTORS . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .1 X 5.9 H P

ELECTRICS. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .575/60/3 VO LT

FLOOR SPACE DIMENSIONS. . . . . . . . . . . . . . . . .57”x 50”x 87” H

APPROXIMATE WEIGHT.. . . . . . . . . . . . . . . . . . . .3,970 LB

| CONE SERVO-DRIVEN CNC PRESS BRAKES The Cone Model C9 (25 Ton) represents a new generation of servo-electrical press brakes. Built in Finland, they are both servo driven and are equipped with the highest class linear guides. Utilizing the pulley principle, they are specially designed for years of accurate bending under the most demanding requirements. A user friendly programming system makes set-up fast and "hot job" production changes routine. The development of the Cone series has been made with ergonomic design in mind, as well as providing convenient working conditions for the operator who can sit at the machine. These machines are also friendly for our environment, for a servo driven press brake has no oil changes needed, and no waste oil generated to stress our environment. Servo-Driven machines are more energy efficient than hydraulic machines. This is because only the electrical power required for the necessary bending force (tonnage) is consumed for each stroke. The cycle times and maintenance levels are better than a hydraulic press brake. In addition, the cycle times are shorter due to fast back gauging and shorter acceleration time. The faster the cycle time, the quicker the payoff period to justify the purchase of the press brake. There is less energy required to operate and less heat generated. One of the main characteristics of these brakes is the low energy consumption and that can result in up to 50% savings compared to a hydraulic press brake. Overall, the Cone Press Brake is designed to be more ergonomic, economical, and more efficient than conventional bending equipment. |  |
| --- | --- |
|  |  | l |

DESIGN

-- FULL electronic servo-drive press brake.

-- COMPLETE with the OMRON YASKAWA touch screen colour control with

CONE programming software.

-- ROLLER GUIDES are used in the RAM (Y) axis.

-- ELIMINATES mechanical linkages from high load areas where

increased wear and tear will shorten overall life of a machine.

-- ALL controls for the machine are accessible and simple to adjust.

-- GRAVITY assisted ram travel during ram approach for greater

system efficiency.

-- INCREASED ram speed with a reduction in horsepower.

-- LOWER hydro cost and NO hydraulic oil cost or mess.

FRAME

-- WELDED integral frame and bed construction with contoured stress

points assembled from shot blasted steel plate.

-- BED top is smooth with drilled and tapped holes for die holder.

-- DIE HOLDER with drilled & tapped holes for holding vee dies.

-- DEEP THROAT in side frames allows forming over the full length.

-- GREASE LUBRICATION to ram gibbing & screw is standard on all

machines.

-- CNC CONTROL has AUTO-REMINDER for lubrication times.

RAM

-- SOLID one piece steel plate for minimum deflection.

-- RAM is guided by big roller guides on the left and right sides.

-- GUIDES allow ram to always be supported and guided throughout

the stroke length.

-- ADJUSTABLE guides provide lateral stability

-- RAM STRAIGHTENESS is factory set – but can be re-adjusted

by our servicemen quickly and easily.

-- RAM clamp bars are machined for tools with a safety

Tang.

MOTOR CONTROLS

-- STANDARD with on/off switch with a low voltage control circuit.

-- ELECTRIC FOOT SWITCH with TWO operations; NORMAL PRESSING will

begin the pressing operation; BOTTOM PRESSING will activate ram

return (up) procedure.

STROKE CONTROL SELECTIONS

-- EMERGENCY STOP BUTTON on front CNC Control Panel.

-- RESET BUTTON on front CNC Control Panel.

-- AUTOMATIC & SEMI-AUTOMATIC MODES - All Stroke Control Selections are

functional with the Foot Switch from the CNC control.

OMRON TOUCH SCREEN CONTROL

-- MULTI axes control – Y, X, R;

-- COLOUR GRAPHIC LCD SCREEN – 6.75” x 5.5”

-- AUTOMATIC bend allowance calculations generated

from tooling and material information.

-- AUTOMATIC tonnage calculations with manual override.

-- MEMORY CAPACITY which allows storage of up to 250 x 8 Bend

Programs or 125 x 16 Bend Programs or any mix.

-- PROGRAMMABLE ram approach speed, pressing & return speeds.

-- PROGRAMMABLE ram dwell at bottom of stroke.

-- PROGRAMMABLE stroke length.

-- PROGRAMMABLE back gauge retract distance and delay.

-- PROGRAMMABLE bump form.

-- PROGRAMMABLE back gauge return speed.

-- INCH/METRIC programming.

-- PART counter.

-- DIRECT angle programming in degrees or mm.

-- TOOL STORAGE – up to 50 dies and 50 punches along with

safety zones can be saved in memory with a 10 numbered

alpha-numeric listing.

-- ALPHA-NUMERIC (10)listing in memory for each program saved.

-- MATERIAL LIBRARY.

-- PRODUCTION TIME indicator.

-- STANDARD Ethernet port.

-- OPTIONAL SOFTWARE: For easy backup via Network.

- Directory creation to server from Press Brake.

- Upload/Download from Press Brake.

- Directory hierarchy support for storing Each Customer’s

Programs In His own Folder.

QUOTATION

ONE ONLY NEW CONE SERVO-DRIVEN CNC  PRESS BRAKE

MODEL: CONE C9 – 34” X 25 TONS

C/W: - ALL STANDARD ITEMS AS PER OUR LITERATURE AND QUOTATION;

- OMRON CNC TOUCH SCREEN COLOUR CONTROL;

- 3 AXES – Y (PROGRAMMABLE RAM DEPTH)

X (CNC 15.75” HIGH SPEED BACK GAUGE C/W: 2 FINGERS);

R (CNC PROGRAMMABLE HEIGHT TO BACK GAUGE)

- AMADA STYLE TOP & BOTTOM TOOL HOLDERS;

- ONE ELECTRIC FOOT PEDAL WITH SAFETY LIMIT SWITCH;

- 575/60/3 VOLT CSA ELECTRICS & ELECTRICAL SAFETY APPROVAL;

- LASER-SAFE GUARDS ALLOW OPERATOR TO WORK CLOSE TO DIES AND

ENABLES BOX BENDING IN SLOW SPEED MODE.

- SIDE SAFETY FENCES, REAR SAFETY GATE, CLASS 4 SAFETY SYSTEM C/W:

SAFETY RELAY IN PANEL, READY FOR PSR;

F.O.B. . . . . . . . . .YOUR PLANT DOOR

INSTALLATION. . . . .TRAINING INCLUDED

TAXES . . . . . . . . .EXTRA WHERE APPLICABLE.

DELIVERY . . . . . . .8 - 10 WEEKS

TERMS . . . . . . . . .35% WITH ORDER;

. . . . . . . . .BALANCE NET 30 DAYS FROM DELIVERY;

*********************************************************************

PRICE. . .$70,500.00 CDN

*********************************************************************

-- STEVENS MACHINERY will provide a serviceman to train operator(s)

and maintenance men in your factory. We will initially be spending

2 – 3 days training and will be available after for any questions

You may have for programming or operation.

WARRANTY

STEVENS MACHINERY SALES INC & COASTONEOY INCLUDE A ONE YEAR WARRANTY

ON THIS NEW MACHINE FOR PARTS AND SERVICE SUBJECT TO PROPER TOOLING BEING USED IN THE MACHINE AND USAGE BY A FACTORY TRAINED OPERATOR.

OPTIONS

1.  575/60/3 VOLT CSA ELECTRICS & HYDRO APPROVAL    - INCLUDED

2.  LASER-SAFE GUARDS ON FRONT OF MACHINE           - INCLUDED

3.  NON-REPEAT SAFETY STYLE FOOT PEDAL              - INCLUDED

4.  SIDE & REAR FENCE WITH SAFETY INTERLOCKS        - INCLUDED

5.  R AXIS (5.50” HEIGHT TO BACK GAUGE)             - INCLUDED

6.  AMADA STYLE TOP & BOTTOM TOOL HOLDERS           - INCLUDED

7.  COMBI NORTH AMERICAN & AMADA TOOL HOLDERS       - $2,325.00 CDN

8.  WILA STYLE TOP & BOTTOM TOOL HOLDERS            - P.O.R.

9.  LARGER 15” OMROM CNC DISPLAY SCREEN             - $1,850.00 CDN

10. SWING ARM FOR FOR LARGER DISPLAY SCREEN         - $1,050.00 CDN

11. EXTRA BACK GAUGE FINGERS                        - $450.00 CDN EACH

12. INCREASE TONNAGE FORCE BY 20%                   - $2,100.00 CDN

13. Z1 & Z2 MOVEMENT OF BACK GAUGE FINGERS          - $6,550.00 CDN

14. DELTA X (+/- 2”) MOVEMENT OF ONE FINGER         - $4,500.00 CDN

15. TWO FRONT SHEET SUPPORT ARMS ON LINEAR GUIDES   - P.O.R.

16. EXTRA OPEN HEIGHT UP TO 31.4” – X MODEL         - P.O.R.